## Slide 1
Constructive Computer Architecture
Virtual Memory:
From Address Translation to Demand Paging
Arvind
Computer Science & Artificial Intelligence Lab.
Massachusetts Institute of Technology

## Slide 2: Modern Virtual Memory Systems Illusion of a large, private, uniform store
Protection & Privacy
  Each user has one private and one or more shared address spaces
page table  name space
Demand Paging
  Provides the ability to run programs larger than the primary memory
  Hides differences in machine configurations
The price of VM is address translation on each memory reference
OS
useri
VA
PA
mapping
TLB
Swapping Store
Primary
Memory

## Slide 3: Names for Memory Locations
Machine language address
  as specified in machine code
Virtual address
  ISA specifies translation of machine code address into virtual address of program variable (sometime called effective address)
Physical address
  operating system maps virtual address into physical memory addresses
physical
address
virtual
address
machine
language
address
Address
Mapping
ISA
Physical Memory
(DRAM)

## Slide 4: Paged Memory Systems
Processor generated address can be interpreted as a pair <page number, offset>
A page table contains the physical address of the base of each page
Page tables make it possible to store the pages of a program non-contiguously
0
1
2
3
Address Space
of User-1
Page Table
of User-1
0
1
2
3
1
0
2
3
page number offset
Page (4kB)
Page descriptor (4-8B)
Notes: Relaxes the contiguous allocation requirement.

## Slide 5: Private Address Space per User
VA1
User 1
Page Table
VA1
User 2
Page Table
Physical
Memory
free
OS
pages
free
Each user has a page table which contains an entry for each user page
System has a “Page” Table that has an entry for each user (not shown)
There is a PT Base register which points to the page table of the current user
OS resets the PT Base register whenever the user changes; requires consulting the System Page Table

## Slide 6: Suppose all Pages and Page Tables reside in memory
VPN offset
PT User 1
PT User 2
System PT Base
PTB Useri
+
Translation:
  PPN = Mem[PT Base + VPN]
  PA = PPN + offset
All links represent physical addresses; no VA to PA translation
On user switch
  PT Base Reg := System PT Base +
  new User ID
System PT
PT Base Reg
It requires two DRAM accesses to access one data word or instruction!
Virtual Page Number
Physical Page Number

## Slide 7: VM Implementation Issues
How to reduce memory access overhead
What if all the pages can’t fit in DRAM
  What if the user page table can’t fit in DRAM
  What if the System page table can’t fit in DRAM
A good VM design needs to be fast and space efficient
Beyond the scope of this subject

## Slide 8: Page Table Entries and Swap Space
VPN
Offset
Virtual address
PT Base Reg
Data word
Data Pages
Offset
All the pages of all the users may not fit in DRAM and therefore, DRAM is backed up by swap space on disk (Disk is not shown)
Page Table Entry (PTE) contains:
  A bit to indicate if the page exists
  PPN (physical page number) for a memory-resident page
  DPN (disk page number) for a page on the disk
  Protection and usage bits
VPN
PPN
PPN
DPN
PPN
PPN
PPN
Page Table
DPN
PPN
DPN
DPN
DPN
PPN

## Slide 9: Translation Lookaside Buffers (TLB)
VPN offset
physical address
PPN offset
virtual address
V R W D tag PPN
hit?
Exception?
Mode = Kernel/User
Op = Read/Write
Protection
Check
TLB
Keep some of the (VPN,PPN) translations in a cache (TLB)
  No need to put (VPN, DPN) in TLB
Every instruction fetch and data access needs address translation and protection checks
TLB miss causes an access to the page table to refill the TLB
Notes: 3 memory references
2 page faults (disk accesses) + ..
Actually used in IBM before paged memory.

## Slide 10: TLB Designs
Typically 32-128 entries, usually fully associative
  Effectively no spatial locality across pages
  Large TLBs (256-512 entries) are usually 4-8 way set-associative
Switching users is expensive because TLB has to be flushed
Handling a TLB miss: “Walk” the page table; if the page is in memory, reload the TLB otherwise cause a page fault, i.e., missing-page exception
  page faults are always handled in software
  but page walks are usually handled in hardware using a memory management unit (MMU)
    RISC-V has no TLB miss exceptions and thus, mandates hardware MMU
Sometimes TLB entries contain User IDs
Notes: To avoid flushing TLB on a user change

## Slide 11: TLB Reach
The size of largest number of physical pages that can be accessed via a TLB
  Example: 64 TLB entries, 4KB pages, one page per entry
  TLB Reach =
64 entries * 4 KB = 256 KB
==> many DRAM resident pages can’t be accessed without a TLB refill
small relative to typical DRAM size
Use several different page sizes (4KB, 2MB, 1GB, ...), i.e., use TLB entries more efficiently
  Each size, requires a different split of a virtual address into (VPN, Offset)
Fast TLB refills for DRAM-resident pages by doing the refills in hardware
solutions
Notes: To avoid flushing TLB on a user change

## Slide 12: Handling a Page Fault
When the referenced page is not in DRAM:
  The missing page is located (or created)
  It is brought in from disk, and page table is updated
    Another job may be run on the CPU while the first job waits for the requested page to be read from disk
  If no free space left in DRAM, a page has to be swapped out using some replacement policy
    Popular policy “approximate LRU”
Since it takes a long time (msecs) to transfer a page, page faults are handled completely in software (OS)

## Slide 13: Address Translation: putting it all together
Virtual Address
TLB
Lookup
Physical
Address
(to cache)
miss
hit
Page Table
Walk
the page is
Ï memory Î memory
Protection
Check
denied
permitted
hardware
hardware or software
software
Protection
Fault
Seg fault
Update TLB
Resume the instruction
Page Fault
(OS loads page)
Where?
Notes: Need to restart instruction.
Soft and hard page faults.

## Slide 14: RISC-V Virtual Memory Privileged ISA v. 1.9.1

## Slide 15: RISC-V Privilege Levels
Needed for protection – User programs can’t exercise some hardware capabilities
  User-mode (U) – addresses are virtual, access to devices only through system calls
  Supervisor-mode (S) – addresses are typically virtual addresses, can switch page-table in use (sptbr)
  Machine-mode (M) – all addresses are physical addresses, has access to all addresses including memory-mapped IO devices
CSR
No VA to PA translation

## Slide 16: RISC-V Memory Maps
DRAM
Boot ROM
MMIO
Debug Unit
Machine-Mode Physical Addresses
DRAM
User-Mode Virtual Addresses
Demand Paging makes the entire address space look like DRAM
Only part of the address space is DRAM

## Slide 17: RISC-V Sv32 Virtual Addressing Mode
Virtual Addresses:
Physical Addresses:
VPN[0]
page offset
VPN[1]
12 bits
10 bits
10 bits
PPN[0]
page offset
PPN[1]
12 bits
10 bits
12 bits
1st level PT Index
2st level PT Index
User PT is organized as a two-level tree instead of a linear table with 220 entries
For large pages, PPN[0] is the page number and the offset is calculated by combing page offset and PPN[1]

## Slide 18: Sv32 Page Table Entries
PPN[0]
SW Reserved
PPN[1]
D
A
G
U
X
W
R
V
2 bits
10 bits
12 bits
Dirty – This page has been written to
Accessed - This page has been accessed
Global – Mapping exists in all virtual address spaces
User – User-mode programs can access this page
eXecute – This page can be executed
Write – This page can be written to
Read – This page can be read from
Valid – This page valid and in memory

## Slide 19: Sv32 Page Table Entries
If V = 1, but X, W, R == 0, PPN[] points to the 2nd level page table
If V = 0, page is either invalid or in disk. If in disk, the OS can reuse bits in the PTE to store the disk address (or part of it).
Disk Address
G
U
X
W
R
0
26 bits
PPN[0]
SW Reserved
PPN[1]
D
A
G
U
X
W
R
V
2 bits
10 bits
12 bits

## Slide 20: RISC-V Pipeline with VM
PC
Inst TLB
Inst. Cache
D
Decode
E
M
Data TLB
Data Cache
W
+
Page Table Walker
miss
miss
Page Table Walker
translation, page fault or segfault
memory accesses
memory accesses
On a fault, an exception is raised and the OS takes over
translation, page fault or segfault

## Slide 21: SFence.VM Instruction
Privileged instruction to synchronize TLB translation
  Flushes stale TLB translations
  Ensures that stores to data cache are seen by hardware page table walker
A similar instruction (Fence.I) is needed to support self-modifying code

## Slide 22: Final comments
Virtual memory is a an essential feature of almost all processors except for the smallest processors that are used in the embedded space
Significant verification effort is required to boot an Operating system on a processor because of virtual memory
Precise exceptions are essential to implement VM systems
  Performance is usually not an issue, and therefore sometimes exceptions are implemented using microcode